## Slide 1: MockPDK & Analog Router: Getting Started
Nikolay Ryzhenko
Created: October 29, 2018
Last updated: July 3, 2019
DARPA IDEA technical meeting
Training material

## Slide 2: Updates
7/3/2019: (rev 16195): Added a new optional parameter: Tie

## Slide 3: Outline
Origin on the mock process design kit
The layer stack
Basic design numbers and metal templates
PDK files
Format of the files

## Slide 4: MockPDK: Mock Process Design Kit
A process design kit (PDK) is a set of files used to model a fabrication process for the tools used to design integrated circuits.
Disclaimer: A public paper (ISPD 2017) highlights some details of a possible 7nm process. We use a layer stack presented in Figure 1 in our subsequent examples. The original paper has no actual numbers and design rules. In this presentation, mock numbers were selected to keep similar relative shapes of layout objects.
Source: Automatic Cell Layout in the 7nm Era
Pascal Cremer, Stefan Hougardy, Jan Schneider, Jannik Silvanus
Proceedings of the ACM on International Symposium on Physical Design, 2017

## Slide 5: Layer Stack
RX, n-well
Substrate
PC, gate contact
TS, source/drain contact
SF, silicon fin (added acronym)
M0
V0
M1
V1
M2
V2
M3
V3
M4
V4
CA, a via between PC/TS and M0
M5
V5
M6
SF
Source: Automatic Cell Layout in the 7nm Era
Pascal Cremer, Stefan Hougardy, Jan Schneider, Jannik Silvanus
Proceedings of the ACM on International Symposium on Physical Design, 2017

## Slide 6: Basic Numbers: PC, TX, SF, M0, M1, M2
RX
PC
TS
SF
M0
V0
M1
V1
CA
M2
V2
M3
V3
M4
V4
M5
V5
M6
All wires are unidirectional; the orientation is either vertical or horizontal.
Poly (PC) pitch is set to 1000 mock units. Having this, other numbers mimic layouts of the paper such as depicted in Fig.6. The remaining values are set as follows:
TS/M1 fixed pitch = PC fixed pitch: 1000 units
Fin (SF) fixed pitch: 400 units
PC fixed width: 300
TS fixed width: 400
M1 fixed width: 700
PC fixed side-to-side (STS) spacing: 700
TS fixed STS: 600
M1 fixed STS: 300
M0 fixed STS: 300
M0 regular template of widths: {1100, 500, 500, 300, 300, 300, 500, 500, 1100}
M2 fixed STS: 300
M2 regular template of widths: {1000, 900, 600, 600, 600, 900, 1000}
Vias are placed at the intersections of corresponding center-wire grid lines.
Source: Automatic Cell Layout in the 7nm Era
Pascal Cremer, Stefan Hougardy, Jan Schneider, Jannik Silvanus
Proceedings of the ACM on International Symposium on Physical Design, 2017

## Slide 7: Basic Grids: PC, TX, SF
6400
16 fins per row height
FET boundary
Fin
RX
PC
TS
SF
M0
V0
M1
V1
CA
M2
V2
M3
V3
M4
V4
M5
V5
M6

## Slide 8: M0, M1, and M2 templates
M0 template:
Fixed side-to-side spacing (STS): 300
{1100, 500, 500, 300, 300, 300, 500, 500, 1100}
Period: 6400 (16 fins)
M1 template:
Fixed pitch: 1000
Fixed width: 700
Fixed STS: 300
M2 template:
Fixed STS: 300
{1000, 900, 600, 600, 600, 900, 1000}
Period: 6400 (16 fins)

## Slide 9: MockPDK: All available metal templates
M0:
  {1100, 500, 500, 300, 300, 300, 500, 500, 1100}, STS=300
M1:
  {700}, STS=300
M2 templates (two options):
  {1000, 900, 600, 600, 600, 900, 1000}, STS=300
  {500}, STS=300
M3:
  {800, 600, 400, 400, 400, 600, 800}, STS=300
M4:
  {800, 600, 400, 600, 800}, STS=400
M5:
  {1000, 800, 600, 600, 600, 800, 1000}, STS=400
M6:
  {1600, 1200, 1000, 1200, 1600}, STS=400
Black values have been chosen to mimic layouts from a paper:
Automatic Cell Layout in the 7nm Era
Pascal Cremer, Stefan Hougardy, Jan Schneider, Jannik Silvanus
Proceedings of the ACM on International Symposium on Physical Design, 2017
Green values are arbitrary mock numbers.

## Slide 10: Detailed Router Collateral
Process collateral:
  layers.txt - technology layers
  design_rules.txt - numeric values for primary design rules
  via_generators.txt - geometries and names of available vias + metal enclosures
  patterns.txt - forbidden layout patterns for vias
  metal_templates.txt - available metal templates
Circuit-specific collateral:
  mtis.txt - a list of active metal template instances
  netlist.txt - cell name, bounding box, and input wires
  globalrouting.txt - connected entities and global routes
Flow and execution:
  arch.txt - a list of synthesis options
  file.txt - run file

## Slide 11: Layer file: layers.txt
The file describes all layers. Almost all fields are optional. However, correct layer specification for any PDK must have a strict number of consistent parameters.
The only mandatory field
All entries are optional
Optional
Layer name=<STRING> pgd=hor|ver level=<INT> {
Type value=well|diffusion|wire|poly|via|metal
Technology pitch=<INT>
ElectricallyConnected layer=<STRING>
Color type=<STRING> name=<STRING>
}

## Slide 12: Tips for the layer file
Need to specify both the diffusion pitch and the poly pitch because they define the global routing grid.
Layers which are not used for routing don’t need a level. For example, well and diffusion.
Carefully set levels for vias and wires.
Levels, orientation, types, and electrically connected layers are used to guide the router.
The router doesn’t have any hardcoded information about layers. The router doesn’t interpret names of layers anyhow.

## Slide 13: Design rules: design_rules.txt
The file defines a few primary design rules. Examples:
minete is a minimal spacing between wire line-ends (“minimal end-to-end“)
minlength is a minimal wire length
Rule name=<STRING> type=minete value=<INT> layer=<STRING>
Rule name=<STRING> type=minlength value=<INT> layer=<STRING>
Example:
minete
Horizontal metal wire
Horizontal metal wire
minlength
line-end, edge
side
OGD
orthogonal grid direction for a horizontal layer
PGD
primary grid direction for a horizontal layer

## Slide 14: Via generators: via_generators.txt
A via generator is a set of several wires: a via cut, a metal landing (layer below), and a metal enclosure (layer upper). Format is a bit awkward. Some fields are upper-case, other fields are lower-case. It was made to keep a backward compatibility with another old and user-unfriendly format. x_coverage and y_coverage can be zero or even negative. Widths is a list of wire widths where this via type is allowed to be landed. All numbers are FLOAT (are to be multiplied by 10,000 to get actual integer units).
Generator name=<STRING> {
Layer1 value=<STRING>
x_coverage value=<FLOAT>
y_coverage value=<FLOAT>
widths value=<FLOATs>
}
Layer2 value=<STRING>
x_coverage value=<FLOAT>
y_coverage value=<FLOAT>
widths value=<FLOATs>
}
CutWidth value=<FLOAT>
CutHeight value=<FLOAT>
cutlayer value=<STRING>
}
Example:
500
460
100: Layer2: y_coverage
20: Layer1 y_coverage
M2
V2
M3

## Slide 15: Layout pattern: patterns.txt
Layout patterns are used to model forbidden layout cases. Right now, vias are supported best of all. Any arbitrary function can be expressed: any width, any depth. “mbp” stands for “must be present”. “mba” stands for “must be absent”. While you have a finite list of metal templates, you need to enumerate all possible forbidden via layouts. If you have very few regular and uniform templates, the number of patterns is really small.
Example
Design rule: Corner-to-corner spacing between vias
Pattern: Forbidden “diagonal” placement of two vias.
Pattern name=<STRING> shortname=<STRING> comment=“any arbitrary comment”
Node type=AND|OR|NAND|NOR {
Node type=leaf pr=mbp|mba layer=<STRING> rect=<xl>:<yl>:<xh>:<yh>
}
}
via1
via1
0
660
1000
1660
0
460
800
1260

## Slide 16: Metal templates: metal_templates.txt
MetalTemplate layer=<STRING> name=<STRING> widths=<INTs> spaces=<INTs> colors=<STRINGs> stops=<INTs>
Metal2 in this MockPDK has two available templates. All other metals have one available template.
A list of available metal templates is technology information. Circuit may use 1+ of available metal templates.
You may specify a custom list of side-to-side spaces separated by commas.
Stops define fixed stopping points for wire line-ends.
Mandatory fields:
layer
name
widths
spaces (side to side spacing)
Optional fields:
colors (default: “”)
stops (default: “”)
Metal template is a repeating fixed set of wire widths and side-to-side spaces.

## Slide 17: Metal templates instances: mtis.txt
4 MTIs define a m2 routing region m2_template_00 {1000, 900, 600, 600, 600, 900, 1000} with a rectangular hole in the middle.
The last M2 MTI defines a rectangular routing region m2_template_01 {500, 500} in the middle of the block.
MetalTemplateInstance template=<STRING> pgdoffset_abs=<INT> region=<xl>:<yl>:<xh>:<yh> inverted=1|0
500
pgdoffset_abs defines the offset of the first wire track with respect to the PGD grid line at point (0,0).
An example is shown for M1.
(0,0)
m1_template_00
38400
89600
0
128000
m2_template_01, pgdoffset_abs=0
m2_template_00, pgdoffset_abs=0
Mandatory fields:
template
Optional fields:
pgdoffset_abs (default: 0)
pgdoffset_rel (default: 0)
region (default: bbox)
inverted (default: 0)
A list of metal template instances (MTIs) is usually custom for a given circuit.

## Slide 18: Input file: netlist.txt
The file defines a rectangular bounding box of the cell and a list of input wires. Hierarchy is not supported yet; layout is flat. A special format specifies what wires should be connected and how. See the next foil.
Cell name=<STRING> bbox=<xl>:<yl>:<xh>:<yh>
Wire net=<STRING> layer=<STRING> rect=<xl>:<yl>:<xh>:<yh> gid=<INT>
An unique Global ID, an optional integer
See the next foil for more details
Example:

## Slide 19: Connected entities and GR: globalrouting.txt
Connected entity is a list wires which are supposed already connected even these wires may look unconnected. The detailed router connects connected entities rather than input wires. Global routes define global routing. Global route (GR) must be either vertical of horizontal; net, coordinates, and layer are mandatory. Minimal width of GR is optional.
ConnectedEntity terms=<list of GIDs>
GlobalRouting net=<STRING> routes=(<xl>,<yl>,<xh>,<yh>,<layer>,minw=<INT>,gid=<INT>,samewas=<INT>); . . .
Minimal width for this route
Uncritical routing: no target minimal width
Integers are GIDs (wire’s global IDs).
Unique GR id
“same width as” another GR gid
Target minimal width

## Slide 20: Tie: globalrouting.txt
Tie is an optional parameter that assigns a terminal wire to a global routing segment. Both the terminal and the GR segment must have an unique integer gid. Ties improve correlation between GR and DR. Ties reduce the solution space and significantly reduces the runt time. By default (without ties), DR creates all possible routes between terminals and all GR segments around.
A tie can bind only a terminal wire and a GR segment. A tie cannot bind two terminal wires. A tie cannot bind two GR segments.
Tie term0=<terminal gid> gr0=<GR gid>
For example:
ConnectedEntity terms=7587
GlobalRouting net=n0 routes=(2,4,23,4,metal2,gid=849)
Tie term0=7587 gr0=849

## Slide 21: Options: arch.txt
Some synthesis options are stored in a separate file. Following two options define global routing grid.

## Slide 22: Run file: file.txt
A minimal list of options:

## Slide 23: How to run
amsr.exe -file file.txt